## Slide 1
TEST DEVICE FOR HUMAN OCCUPANT RESTRAINT
THOR-50M - 50TH PERCENTILE MALE
1992
TAD-50M
Prototype
2001
THOR Alpha
2005
2011
THOR
Mod Kit
2014
THOR
Metric
THOR-NT
2015 - Present
History
What?
Why?
Anthropomorphic Test Device (ATD, or crash test dummy)
Represents male of average height and weight
Designed for frontal and frontal oblique crash tests
Measures risk of injury to occupants in a crash
Used in hundreds of NHTSA research tests
THOR’s human-like characteristics in a crash and state-of-the-art measurement capability make it the best choice to evaluate the advanced safety features in today’s vehicles.
Human-Like Characteristics
• Neck that bends, twists, and stretches for realistic head motion
• Torso with anatomically correct ribcage and shoulder
• Flexible spine to allow proper upper body motion
• Abdomen and pelvis that mimic human seat belt interaction
• Legs that respond to impact of dashboard and pedal
Measurement Capability
Over 100 distinct measurements to help predict injury, including:
• Head acceleration and rotation
• Neck forces and moments
• Ribcage motion at four locations and three dimensions
• Abdomen motion at two locations and three dimensions
• Pelvis, thigh, shin, and ankle forces
THOR-50M
More information at
https://www.nhtsa.gov/biomechanics-trauma/thor#thor-male
THOR-50M
H3-50M
from Lobdell, 1973
Biofidelity
Body Region | THOR-50M | H3-50M
Head | Excellent | Poor
Neck | Good | Poor
Thorax | Excellent | Good
Abdomen | Marginal | Marginal
Knee/Thigh/Hip | Good | Poor
Lower Extremity | Good | Excellent
Whole-body | Good | Good
Application in NHTSA Research Projects
Parent, D., Craig, M., Moorhouse, K., “Biofidelity Evaluation of the THOR and Hybrid III 50th Percentile Male Frontal Impact Anthropomorphic Test Devices,” 61st Stapp Car Crash Conference, November 2017.
Assessing Occupant Protection for Automated Vehicles
Oblique Restraint Countermeasures
Vehicle FE Model Development
Repeatability & Reproducibility
Enhancements
Finite Element Model
Allows virtual crash tests, parametric analyses
Developed by NHTSA with support from academic and industry partners
Current work (University of Virginia Center for Applied Biomechanics)
  Update hardware to current drawing package
  Match response to current qualification specifications
  Improve computational efficiency and stability
Qualification Tests
Crash Tests
24
Test Modes
e.g. Face Impact, Neck Torsion
Left Thorax, Right Ankle
5
Tests per ATD
5
ATDs
3 ATDs at VRTC
1 ATD at 2 other labs
×
×
=
600
Qualification
Tests
 Qualification Specifications (Mean ±10%)
 Assessment of Repeatability and Reproducibility:
3
Test Labs
3
Tests per Lab
×
=
9
Oblique Crash Tests
Shape
Magnitude
Phase
  Saunders et al., 2018 SAE World Congress
In-dummy Data Acquisition System (DAS)
Improved 3D thorax and abdomen measurement
Vehicle Crash Tests
164
Crash Simulation Sled Tests
348
Dynamic Component Tests
1013
THOR-50M ATDs owned by NHTSA, used in:
8
32,604
Sensors
Data collected in these tests accounts for:
282 Million
Data Points
Data, photos, videos, and test reports are available to the public in the NHTSA Biomechanics and
NHTSA Vehicle Crash Test Databases: https://www.nhtsa.gov/research-data/databases-and-software